## Slide 1
River navigation
Engineering
&
ELISE RATCLIFF, NATURAL RESOURCE SPECIALIST

## Slide 2
Historical problems, Modern solutions
In the 1800’s, the Mississippi River was only about 3 feet deep on average
  Boats frequently got stuck or damaged on snags and sandbars
  Average lifespan of a steamboat = only 18 months!
In the 1930’s, Congress tasked the USACE with dredging and maintaining a 9-foot navigation channel
  A system of locks and dams was put into place to help maintain ideal river depth
Principle 1: Protect People from Water
Principle 3: Make Water Useful!

## Slide 3
How dams work
Water is held back by tainter gates
  Curved gates that swivel on a pivot
  Can be raised to let more water through, or lowered to hold more back
  Dams on the Mississippi typically consist of multiple tainter gates in a row
The area behind a dam is called its pool
  We are Locks and Dam 26; the water immediately upstream of us is Pool 26
  Each dam controls the level of the water upstream of it

## Slide 4
How dams work
29 lock and dams were constructed on the upper Mississippi River from Minneapolis to Granite City, IL
  South of Lock 27 is open river
  Confluence of Missouri with the Mississippi brings enough water to maintain depth without dams
Because there is significant elevation change from the mouth of the Mississippi to the Missouri Confluence, multiple dams are needed to account for the gradual change in depth
This creates a stair-step effect
  Locks become necessary to move boats through the dam
    - “Elevator” for boats to get from one water level to the next

## Slide 5
How Locks work
  Miter gates (or lift gate) open
  Boat moves into the chamber and ties up on the side
  Lock chamber is filled or drained through pipes in the lock walls
    If going upstream, water level is raised. If downstream, water level is lowered
    Water movement is passive via gravity rather than pumped
  Gates open, boat unties and continues on its way
This design is more typical of older locks – Melvin Price has multiple lock chambers and a control tower up above

## Slide 6
Rivers Project
  The Rivers Project Office operates and maintains the last stretch of navigation channel
    4 Dams and 5 Locks
    3 Motor Vessels
      Dredges help maintain the depth of the riverbed

## Slide 7
hydropower
USACE is the largest generator of hydropower in the US
  75 power-producing dams housing 356 individual generating units
  25% of the nation’s hydroelectric power
  More than 70 billion kilowatt hours per year
    Enough to power 10 cities the size of Seattle!

## Slide 8
hydropower
Melvin Price is not a hydropower dam (not enough elevation change)
8 non-federal plants (private or municipal) on the Mississippi River use USACE dams to generate power
  4 USACE-owned plants at reservoirs within the Mississippi Valley Division
    Clarence Cannon, MO
    Narrows, AR
    Blakely Mountain, AR
    DeGray, AR

## Slide 9
How hydropower
works
Potential Energy
Kinetic Energy
Electricity

## Slide 10
Parts of a turbine
Penstock
  Big pipe that directs the water flow
Turbine blades
  Water moves the blades, which turn the shaft
Shaft
  Connects the turbine to a generator
Generator
  The spinning shaft turns a rotor, producing electricity
Water flow
  Water that returns to the river

## Slide 11
Let’s make a turbine!

## Slide 12
Let’s make a turbine!
Objective:
  Build a water wheel that can lift a paperclip from the bottom of the container to the water wheel shaft
Supplies:
  Foam cup
  Small medicine cups
  Big spoons
  Little spoons
  Straw
  Tape
  Lid

## Slide 13
Let’s make a turbine!
Steps:
Take 2 minutes to discuss your design as a team
Send 1 teammate to gather all supplies from front table
  Plastic Tub
  Straw
  String
  Paper Clip
  Binder Clip
Construct your design ~20 minutes
Once you have completed your design, come to the front testing area to test your device!
Redesign as needed

## Slide 14
In the classroom
This is a versatile activity that can be tailored to a variety of age ranges
  Additional challenges for older students can include adding or removing materials, changing the flow rate of the water, and asking them to hypothesize what might happen when variables are changed
Potential questions:
  What about your hydroelectric power generator design worked successfully?
  What about your hydroelectric power generator design did not work?
  If you were to return to the design process, how would you change your design to make your water wheel more effective?
  How does your model compare with what you know of large-scale hydroelectric generators?
  What are the advantages and disadvantages of using hydroelectric power?